Rcal Products Image Processor

The Rcal Products Image Processor can locate and track moving objects and objects of a set color or brightness. They can also be located based on width, height, aspect ratio, size, and general location. The specifications can be changed via a computer or by using the buttons and potentiometer on the front of the product. The Rcal Products Image Processor provides 2 analog and 2 digital outputs to be used in a robot's code, along with 2 analog and 2 digital inputs to adjust the device with a computer. It has a 51mm by 71mm, color LCD display on the front. An 8mm square camera is located on the back, along with a tri-color LED, and 2x10 pin programming header. It contains an Ethernet connection, a USB connection, and FRC Expansion board cable connection.

Using the Menu

Buttons
Press Button 1 to reach the main menu after the product has been powered on.
Buttons 2 and 3 are used to scroll through options and change the settings.
Buttons 1 is used to select modes and settings so that they can be altered, and to save the settings created.
By pressing buttons 2 and 3 simultaneously, you can exit the menu.

Potentiometer
Once the mode is selected, you can scroll through the modes until you come to “Pot Input.” select it and scroll the through the options. Whichever option is selected is what the potentiometer will adjust.

Selecting a Mode

Press button 1 after it turns on. A description of each mode will appear on the LCD in blue. Press button 1 again to edit the mode. It should highlight red. Then scroll through the modes. When you have arrived at the desired mode, press button 1 to select. The text should then change back to blue to demonstrate selection.

Changing the Mode

If you are not in the menu, press button 1 to take you there. Once in this menu, scroll through the settings of the previous mode until the top of the screen reads “Detect Mode” Press button 1 to change the mode. It will then highlight red and allow you to select a new mode. Press button one to select your new mode. The text should then change back to blue to demonstrate the selection.

 What is Being Detected?

The objects that are detected as being the set color, luminesce, aspect ratio, or movement will be highlighted blue. Red boxes will appear around objects that are detected but don't fit the setting criteria. A set of white cross-hairs will appear in the center of all the objects that fit the settings. A set of green cross-hairs will appear in the center of and a green box that will surround the object that best matches the settings.

Mode Functions

Red/Green/Blue Level
These serve to locate an object of the selected color. The color and intensity of the tri-LED can be used to tint objects and to counteract any tinting done by outside sources.

Motion
This mode can be used to detect and track moving objects across the screen. By using the threshold, you can adjust the speed of the object being searched for.

Luminesce
This mode can be used to detect objects that are lit up or reflective.

Settings
Settings are used to narrow down the selection of objects that fit the basic mode's criteria to improve accuracy.

Turning off settings
The lower the tolerance level, the more selective the filter will be. You can turn off any setting by setting its tolerance level to 100%

Score Tolerance

“Score Tolerance” refers to the score calculated by the accuracy to the values of “Target X,” “Target Y,” and “Target Aspect.” It helps to locate only the objects that fulfill all of the criteria in each of the three settings. This can be used to locate a certain object at a certain distance from the camera. “Score Tolerance” is used to adjust the accuracy of the selections.

Once the mode is selected, scroll through the settings. Find the setting called “Score Tolerance” and select it. Adjust the percentage up and down to select accuracy and then set it.

Mode Accuracy

The accuracy of the basic mode is adjusted through its threshold. Threshold is the minimum intensity of a color, luminosity or movement in order for it to be detected. This can be used to filter out objects that are only a little red, blue, green, bright or moving only slightly.

Once the mode is selected, scroll through the settings to find the setting called “Threshold” This adjusts minimum intensity of the objects being detected. Select it and adjust the minimum intensity that object would have. Then set it.

Detecting Width

By using “Target X” you can adjust the width of the items detected. By using this you can narrow down the possible object matches to only those whose widths take up a certain percentage of the screen. Because this is implemented by the percentage of the screen the width takes up, thin objects close to the camera will be viewed as equivalent to wide objects far away.

Once the mode is selected, scroll through the settings to find the setting called “Target X.” This adjusts the width of the objects being detected. Select it and adjust the percentage of the screen that the width of the desired object would take up. In order to calibrate it, place the desired object at the desired distance from the camera. Adjust percentage up and down until the target object is surrounded by a green box. Then set it. To adjust the accuracy, press button 2 to scroll up to “X Tolerance.” Select it and adjust the accuracy. Once the desired accuracy has been achieved, set it.

Detecting Height

By using “Target Y” you can adjust the height of the items detected. By using this you can narrow down the possible object matches to only those whose heights take up a certain percentage of the screen. Because this is implemented by the percentage of the screen the height takes up, short objects close to the camera will be viewed as equivalent to tall objects far away.

Once the mode is selected, scroll through the settings to find the setting called “Target Y.” This adjusts the heigth of the objects being detected. Select it and adjust the percentage of the screen that the height of the desired object would take up. In order to calibrate it, place the desired object at the desired distance from the camera. Adjust percentage up and down until the target object is surrounded by a green box. Then set it. To adjust the accuracy, press button 2 to scroll up to “Y Tolerance.” Select it and adjust the accuracy. Once the desired accuracy has been achieved, set it.

Detecting Location

“Target Area X Center” and “Target Area Y Center” are used to only select objects in a certain area of the screen. This can be used to find objects that will always be off the ground, or to center and object in the camera sights.

Limiting X

Once the mode is selected, scroll through the settings. Find the setting called “Target Area X Center” and select it to adjust the left to right orientation. Adjust the percentage to the desired location, 0% being all the way to the left and 100% being all the way to the right. Then set it. Press button 2 to scroll up and select “Area X Center Tol.” Adjust the tolerance to the desired level and set it.

Limiting Y

Once the mode is selected, scroll through the settings. Find the setting called “Target Area Y Center” and select it to adjust the up and down orientation. Adjust the percentage to the desired location, 0% being all the way to the bottom and 100% being all the way to the top,then set it. Press button 2 to scroll up and select “Area Y Center Tol.” Adjust the tolerance to the desired level and set it.

Detecting Size

This can be used to find objects of a specific size. However, the size is determined based on the percentage of the screen the object takes up. For example, small objects close to the camera would be viewed as equal to large objects that were far away.

Once the mode is selected, scroll through the settings to find the setting called “Target Area.” This adjusts the size of the objects being detected. Select it and adjust the percentage of the screen that the desired object would take up. In order to calibrate it, place the desired object at the desired distance from the camera. Adjust percentage up and down until the target object is surrounded by a green box. Then set it. To adjust the accuracy, press button 2 to scroll up to “Area Tolerance.” Select it and adjust the accuracy. Once the desired accuracy has been achieved, set it.

Turning on the LEDs

This product has the ability to tint the camera's surroundings with the use of a tri-color LED. This is designed to aid in the detection of specific objects as well as counter-acting any tint of the lighting in the room.

Scroll through the Main Menu. Once you have located the desired LED, select it. Then adjust the intensity of the LED. Once the desired level is reached set it.