MXP Daughter Board

Rcal Products

Sensor Connections
DIO4, DIO7, DIO7, and DIO6 are the connections for sensor inputs (Fig1). These sensors can be connected to either 5v or 12v. To connect a sensor to 5v, put a jumper across the two, corresponding, topmost pins (Fig 2). To connect a sensor to 12v, put a jumper across the two, corresponding, bottom-most pins (Fig 3).

Breakout Board Ribbon Cable Connections
Fig 1: Analog Breakout
Fig 2: Digital Breakout
Fig 3: CPU Expansion Breakout

Fig 4: PWM Outputs

Fig 5: Synchronous Serial Port (SPI Port)

Fig 1: Analog Inputs (0-3)

Analog Voltage
To set the analog voltage to 5v, put a jumper across the two, rightmost pins (Fig 2). To set the analog voltage to 3.3v, put a jumper across the two, leftmost pins (Fig 3).

Fig 4: Analog Outputs (1-2)
These analog outputs can produce 0-5 volts.

Serial Port
Fig 1: P4 RS232 is an asynchronous serial port.
To use the serial port as a 232 serial port, put a horizontal jumper across both levels on the leftmost side (Fig 2).To use the serial port as a TTL serial port, put a horizontal jumper across both levels on the rightmost side (Fig 3).